## Slide 1: Welcome and short summary of upgrade work (LS1)
Mika Masuzawa, Hiroyasu Ego, Makoto Tobiyama
KEK Accelerator Laboratory

## Slide 2: Emergency Assembly Area

## Slide 3
We are here
(3-go-kan)

## Slide 4: The 27th KEKB Accelerator Review
25/Mar/2024 – 27/Mar/2024
https://superkekb.kek.jp/event/135/
https://us02web.zoom.us/j/82433765439?pwd=Y0R3V2dpYTI2a2t5cnlvRXFTY2Ztdz09
  Meeting ID 824 3376 5439
  Passcode 3300
A. Hutton*, R. Rimmer, C. Milardi, F. Zimmermann, E. Perevedentsev*, J. Fox,
J. Seeman, P. Craievich, M. Sullivan, P. Chiggiato, Q. Qin, R. Assmann, R. Tomas,
T. Taylor, K. Oide*
  * Remote

## Slide 5: JFY2024 SuperKEKB operation plan
12
1
2
3
With the inital budget allocated by MEXT, it seems likely that the rings will only be able to operation for three months until July (due to huge electricity costs).
With additional operating budget by KEK, we will be able to operate the rings after summer, maybe 1.5 month.
If there is a supplemental budget from MEXT, it will be possible to operate in March (and probably in December).
Central substation (150MW) switching works.

## Slide 6: Budget for SuperKEKB Project
Same level as JFY2023
  Budget for JFY2023 was extremely tight, in reality.
Chart: JFY2024 Budget
| Electricity cost | Computing (Belle II) | Facility maintenance | Radiation Safety | Belle II | Linac (KEKB) | Ring | Outsourceing (Operators) | Fixed term staff | L He and N2 | Other common use
 | 3462072 | 559295 | 369737 | 148550 | 272196 | 741000 | 699167 | 292271 | 31000 | 39030 | 63532

## Slide 7: Supplemental budget form KEK for anti-aging measures
JFY2023
  Repair of cooling water system, especially inverter system of the pumps.
  Plan have been scaled back and delayed (significantly) due to bidding failures (several times) due to soaring prices and major delays in parts delivery.
  First repairment is scheduled for summer 2024.
JFY2024
  The cost of measure to prevent aging of power supplies and magnets will be taken.

## Slide 8: Human resources (JFY2024)
ACCL 3rd (Head: Kyo Shibata)
  Safety, Vacuum, RF system, ARES cavity, SC cavity, Cryogenics
  Prof: 3, Assoc Prof: 6, Assist. Prof. 3 , Technical Staff: 9, Senior Staff: 9 PD: 2
ACCL 4th (Head: Makoto Tobiyama)
  Control, Beam Transport, Beam Instruments, Magnet, SC Magnet, Commissioning
  Prof. 3, Assoc Prof. 7 Assist Prof : 5, Technical staff: 9, Senior Staff: 8
ACCL 5th (Head: Hiroyasu Ego)
  Prof. 6, Assoc Prof. 6, Assist Prof. 5, PD 1, Technical Staff: 7, Senior Staff: 11

## Slide 9: Academic Staff

## Slide 10: Technical Staff

## Slide 11: International Collaboration
MNPP-01 (R&D for high energy colliders)
  SLAC, IHEP, CERN, IJCLab, INFN
US-Japan collaboration
  R&D for SuperKEKB and the next generation high luminosity colliders(SLAC, ANL, BNL, FNAL..)
  Development and Study of Superconducting Magnet Upgrades for SuperKEKB(BNL, FNAL)
  etc..
Many young collaborators have been joined the commissioning of the rings after LS1
  Supported by EAJADE program in EU.
  >15 young scientists have been contributing.

## Slide 12
Vacuum works during LS1 at a glance (MR)
HER
Collimator head replacement
(D06V1, D06H3)
Installation of HOM absorber chamber
LER
Injection septum & chamber replacement
NLC (D05V1) system construction
Collimator head replacement
(D05V1)
Collimator relocation
(D03V1 -> D05V1)
Collimator head replacement (D02V1)
Collimator head replacement
(D09V1)
Installation of new bellows chambers with SR masks
Collimator head replacement (D01V1)
Gate valve & bellows chamber replacement
NEG pump feedthrough replacement (Vacuum leak)
Collimator relocation
(D06H1 -> D06H4)
Collimator head replacement
(D06H3, D06H4)
IR works
IR works
Removal and reinstallation of kicker ceramic chambers for magnetic field measurement
: Area open to dry nitrogen or atmosphere
Bellows chamber replacement
(vacuum leak)
Temporary countermeasure against vacuum leak from beam pipe welding line
Ion pump feedthrough replacement
(Abnormal discharge, Vacuum leak)

## Slide 13
Vacuum works during LS1 at a glance (BT&DR)
DR
BT
Removal and reinstallation of Ext. kicker chambers for Kicker PS work
Removal and reinstallation of bellows chambers for magnet alignment (BTe & BTp)
Installation of V-offset bellows chambers (BTp)
Installation of CSR monitor chamber (BTp)
RF cavity work
: Area open to dry nitrogen or atmosphere
Installation of OTR screen monitor (BTp)

## Slide 14: Major upgrade items of LS1
Replacement of damaged collimator heads on both rings.
QCSR cryostat vacuum leak
Aperture enlargement of injection channel and modification of injection final septum of HER.
IR radiation shield modifications.
Non-linear collimator at OHO straight section of LER.
Installment of beam loss monitors/ acoustic sensors/ bunch oscillation monitors to monitor sudden beam loss event.
DR kicker power supply maintenance.
Detailed story will be presented by the individual talks.

## Slide 15
T. Oki

## Slide 16
Aperture enlargement of HER injection channel
Problem of HER injection
  Wall can be an obstacle to injection.
    A wall should be placed between beam channels for stored beam and injected beam.
    Injected beam orbit is too close to the wall.
    High levels of radiation detected at the injection BPM chamber indicates that the injected beam hits the wall.
    It is hard to modify the injection beam orbit.
    ⇒ it is necessary to enlarge the horizontal aperture
    of the injection channel.
M. Kikuchi (2021.12.03)
BITF meeting
wall
No enough room
N. Iida (2022.1.21) BITF meeting
  What is planned during LS1
    Replacement of three beam chambers with new ones.
    Update of injection BPM
    ⇒ More precise injection tuning

## Slide 17
IR radiation shield modification
K. Nakamura
Y. Arimoto
New heavy metal shield on IP bellows
Material change from W to SUS (QCS cryostat front plate)
(Tip of QCS cryostat will be modified to make more space)
K. Nakamura (2022.02.04) 10th SuperKEKB long-term operation plan meeting

## Slide 18: QCS-R re-install
Re-tried on 23/Oct/2023 with
  Modified RVC gear
  Modified VXD cable support
  The QCS supports was carefully advanced by Tanaka-san.
RVC worked very smoothly– no vacuum leak found.

## Slide 19
IR radiation shield modification
Additional concrete shield (IR) & polyethylene shield (Belle2)
  For shielding fast neutrons
    New concrete shields and polyethylene (PE) shield will be added to a space that currently has no shield.
    Additional PE shields around QCS are also planed.
Expected effects of shield modification
  Physics run with wider collimator setting
  Physics run with larger total currents and bunch current
Add PE shields
H. Yamaoka (2021.11.04) IR meeting
PE shield
Add concrete shields
H. Yamaoka (2021.11.04) IR meeting
shield mockup

## Slide 20
NLC construction
collimator
First Sextupole magnet kicks unwanted beam particles.
Second sextupole magnet brings good beam particles back to their original angle.
Collimator scrapes unwanted beam particles with large aperture.
Non-linear collimation scheme (conceptual diagram)
Non-linear collimator (NLC) is being installed in LER Oho straight section.
  Impedance of NLC is much lower than that of conventional collimator due to its large aperture.
  NLC can relax TMCI bunch current limit.
  Oho straight section is the location where the optics satisfies the requirements for NLC.
  A part of wiggler magnets need to be removed.
  New skew sextupole magnets and beam pipes in them need to be fabricated.
  New power supplies, cabling works and new radiation shields are also required.
D05
D04
Oho
straight section
Tsukuba (Belle II)
Positron beam
Oho lab.
collimator
Small aperture can make beam unstable.
Conventional collimation scheme
Quad.
Skew Sext.
Quad.
Skew Sext.

## Slide 21
D05V1
Photo of the non-linear collimator section (2023-05-26)
SNAP.1
(not installed yet)
Σβyky will reduce from 3.97e4 downto 3.18e4 V/pC
Threshold of TMCI is estimated to increase more than 2.mA/bunch
2021c physics run
LS1後
βy*=1 mm
βx*=80 mm
D06V1
D06V1
D05V1

## Slide 22: Nonｌinear Collimator

## Slide 23: Nonlinear Collimator

## Slide 24: Other Collimators
WIGGLER
SuperKEKB Main Ring
e+
e-
HER
LER
IR
e+
e-
TSUKUBA
NIKKO
FUJI
OHO
SC
SC
WIGGLER
ARES
WIGGLER
ARES
ARES
ARES
: Horizontal Collimator, KEKB HER(50x104) type
: Vertical Collimator, KEKB HER(50x104) type
: Horizontal Collimator, SuperKEKB LER(f90x220) type
: Vertical Collimator, SuperKEKB LER(f90x220) type
: Horizontal Collimator, SuperKEKB LER(f90) type
: Horizontal Collimator, SuperKEKB HER(f80x220) type
: Vertical Collimator, SuperKEKB HER(f80x220) type
D01
D02
D03
D04
D05
D06
D07
D08
D09
D10
D11
D12
D02V1
D01V1
D02H1
D05V1
D06V1
D03H1
D02H2
D02H3
D02H4
D01H5
D01H4
D01H3
D06V2
D06H3
D06H4
D09H1
D09V1
D09V2
D09H2
D09H3
D09H4
D09V3
D09V4
D12H1
D12H2
D12H3
D12H4
D12V1
D12V2
D12V3
D12V4

## Slide 25: Status of LER collimator
Name | Type | Tip Material (): longitudinal length in mm | Tip Condition | Remarks
D06H3 | SuperKEKB | Cu coated C (160) | healthy | spoiler against inj. kickers’ accidental firings
D06H4 | SuperKEKB | Ta (10) | healthy | absorber against inj. kickers’ accidental firings
D03H1 | SuperKEKB | W (10) | healthy | 
D02H1 | SuperKEKB | W (10) | healthy | 
D02H2 | SuperKEKB | W (10) | healthy | 
D02H3 | SuperKEKB | W (10) | healthy | 
D02H4 | SuperKEKB | W (10) | healthy | 
D06V1 | SuperKEKB | Cu coated Ti (10) | healthy | 
D06V2 | SuperKEKB | hybrid (3) | healthy | 
D05V1 | SuperKEKB | Cu coated Ta (4) | healthy | 
D02V1 | SuperKEKB | Cu coated Ta (10) | healthy | 

## Slide 26: Status of HER collimator
Name | Type | Tip Material (): longitudinal length in mm | Tip Condition | Drive Mechanism | Remarks
D09H1 | KEKB | Cu coated Ti (40) | damaged |  | 
D09H2 | KEKB | Cu coated Ti (40) | damaged |  | 
D09H3 | KEKB | Cu coated Ti (40) | damaged |  | 
D09H4 | KEKB | Cu coated Ti (40) | damaged |  | 
D12H1 | KEKB | Ti (40) | healthy |  | 
D12H2 | KEKB | Cu coated Ti (40) | damaged |  | 
D12H3 | KEKB | Ti (40) | healthy |  | 
D12H4 | KEKB | Cu coated Ti (40) | healthy |  | 
D01H3 | SuperKEKB | W (10) | healthy | - | 
D01H4 | SuperKEKB | W (10) | healthy | - | 
D01H5 | SuperKEKB | W (10) | healthy | - | 
D09V1 | KEKB | Cu coated Ti (40) | healthy | upgraded | 
D09V2 | KEKB | Cu coated Ti (40) | healthy |  | 
D09V3 | KEKB | Cu coated Ti (40) | healthy |  | 
D09V4 | KEKB | Cu coated Ti (40) | healthy |  | 
D12V1 | KEKB | Cu coated Ti (40) | damaged | upgraded | 
D12V2 | KEKB | Cu coated Ti (40) | damaged |  | 
D12V3 | KEKB | Cu coated Ti (40) | healthy | upgraded | 
D12V4 | KEKB | Cu coated Ti (40) | healthy | upgraded | 
D01V1 | SuperKEKB | Cu coated Ta (10) | healthy | - | 

## Slide 27: Spare jaws
Tip Material (): longitudinal length in mm | Collimator to be installed (assumed) | Remarks
HER vertical: Cu coated Ta (10) | D01V1 | Plan to deliver in this fiscal year.
HER vertical: Cu coated Ta (10) | D01V1 | Plan to deliver in this fiscal year.
HER vertical: Cu coated Ti (40) | D09V1-V4, D12V1-V4 | 
HER vertical: Cu coated Ti (40) | D09V1-V4, D12V1-V4 | 
LER vertical: Cu coated Ta (10） | D02V1 | 
LER vertical: Cu coated Ta (10） | D02V1 | 
LER vertical: hybrid (3） | D05V1, D06V1-V2 | 
LER vertical: hybrid (3） | D05V1, D06V1-V2 | 
LER vertical: Cu coated Ta (10) | D02V1, D05V1, D06V1-V2 | Plan to deliver in this fiscal year.
LER vertical: Cu coated Ta (10) | D02V1, D05V1, D06V1-V2 | Plan to deliver in this fiscal year.
LER horizontal: Ta (10） | D06H4 | 

## Slide 28
Other major works (excluding Linac)
Robust collimator head (LER)
  As countermeasure against kicker-pulser misfiring and resulting destruction of collimator
    Replacement with carbon head of horizontal collimator D06H3 and relocation from D06H1 to D06H4
    Carbon head production :  March 2023
    Head replacement : Spring  Summer 2023
    Collimator relocation : Spring  Summer 2023
New beam pipes with wider aperture at HER injection point
  For injection efficiency improvement
    New beam pipes with wider aperture & New BPM for precise measurement of injected beam
    Beam pipe production :  March 2023
    Beam pipe replacement : Spring  Summer 2023
    Septum baking :  Summer 2023?
RF cavity modification and replacement (LER)
  For stable operation with larger beam current
    Modification : Input coupler replacement, cooling power enhancement, coaxial line modification, etc. (done)
    Cavity replacement (D05A) : January  February 2023
Vacuum seal replacement at RF section (DR)
  For pressure reduction
    Replacement from elastomer gasket to metal gasket for dummy pipes (done)
DR Extraction kicker power supply modification and repair (DR)
  For stable operation
    Modification : December 2022  August 2023
And so on…
MR
Beam pipe at
HER injection point
Y. Suetsugu
Carbon collimator head
T. Ishibashi
DR
DR Ext. kicker
DR RF section

## Slide 29: Injector Linac
Replaced 16 old accelerating structures with new ones (with larger energy gain).
  Starting fabrication of 12 additional accelerating structures
New fast kickers (kick first and second bunch independently), larger aperture pulsed-Qs have been installed.
  Sucessful beam tuning using machine-learning method (Bayesian optimization)
Study of BT beam blowup
  Rejected the CSR-induced beam blowup in positron line
  Still hunting the cause of blowups.
Next step
  Beam diagnostic line at SY3
  BTe-ECS(2024-2025)
  Beam optimization
  etc..

## Slide 34: Summary
Thank you so much for your participation in this 27th KEKB Accelerator Review.
We plan to operate SuperKEKB rings at least 4.5 month.
  2024a 29/Jan to 31/Mar, 2024b 1/Apr to 1/Jul. 2024c 9/Oct to end of Nov.??
  Hoping to receive supplemental operation budget to enable longer operation, especially on Mar/2025.
Accelerator works of Long shutdown 1 was completed almost on schedule and resumed the beam operation.
Please refer to the following presentations for the achievements of this LS1.

## Slide 35: Backup slides