## Slide 1
Injector
F. Miyahara for KEK e-/e+ Injector Linac
Status Report from 2025a to Present and Overview of Upgrades

## Slide 2
Gun Status
Gun#1:Frequent electrical discharges  Improved structure of the 1st cell
RF-Gun#1
RF-Gun#2, 3
Gun#2: Brazed the cavity cells in the wrong order Inner diameter corrected afterward Operated with a shorter pulse width than designed Gun#3: Operated at the designed pulse width. The 2nd bunch is also stable
New Cathode (Thermionic Gun)
Electron Beam
Positron Beam
The charge from the thermionic electron gun gradually decreases (The cause remains unknown)
Cathode was replaced in summer 2025, but the new cathode shows the same trend
Even with an increased heater current, the charge only reaches about 11 nC (a characteristic of this cathode)
Increase the charge by extending the pulse width (2nd bunch only).
There is an issue with satellite bunch generation, but tuning and testing are currently underway.
Detail will be presented in Electron gun/Positron source(Zhou-san’s talk).
Stable operation was achieved during the 2026ab run.
M. Yoshida
Two bunch operation was successfully achieved
Gun#1
Gun#2
Gun#3

## Slide 3
Energy Compression System (ECS)
Four 3-m S-band accelerating structure
Installation was completed during the 2025 summer shutdown.
Due to electrical discharges in the waveguide (caused by a flange issue), operation has been carried out at reduced RF power.
The energy spread in the HER BT has been successfully suppressed.
RF contactors were installed during the 2026 summer shutdown.
RF conditioning and testing are scheduled to begin at the end of October 2026  High RF power
 | 1st only | 1st+2nd | 1st+2nd （energy adjusted） | Requirement
e- | 0.033% | 0.076% | 0.074% | 0.07%
Y. Seimiya
Panel for zero-crossing phase search and accelerating gradient measurement
Current Energy Spread and Required Specifications

## Slide 4
Fast Kicker: Operational use began in the 2026ab run
Y. Okayasu, T. Natsui
Fast Kicker led to stable injection of the second bunch
Orbit correction using the Fast Kicker and Its Effect
A failure occurred in April 2026 Repairs and countermeasures have been completed
Radiation shielding is currently being designed for the area where the failure occurred due to high radiation levels.

## Slide 5
Synchrotron radiation intensity calculation and optics design
  The SRM was designed for installation at bending magnet BM_61_1 in the linac’s 3rd switchyard (SY3), beginning in August 2025
  Synchrotron radiation power on the first HR mirror: ~0.3171 W; no water cooling required (7.0 GeV KBE electron beam)
  Radiation power density is also much lower than in the DR and Main Ring cases
  Single lens imaging configuration
    (Limited by the available space)
    Commercial Achromatic lens: 𝐹# = 10 (Based on the simulation results)
  Remote control of the ND filter wheel and horizontal and longitudinal stages for optimal imaging
  Solid radiation shield is designed for protection of CCD and motorized stages
Beam patterns near focus point
Imaging system layout
R. Zhang, Y. Okayasu
New SR Monitor (SRM_61_1) at SY3 entrance
We plan to incorporate this SR monitor in to the emittance tuning system. Potential applications to the positron beam are also expected.
  Installeld in summer this year
  Synchrotron radiation from a 7 GeV e- beam was successfully observed

## Slide 6
SY3 Beam Diagnostic Line
Energy distribution measurements can be performed by intermittently (1Hz or less) diverting a duplicated KBE (e- for HER) beam mode to the SY3 diagnostic line during normal HER injection operation.
RF phase: Knob to control energy spread
(longitudinal distribution)
The beam energy distribution can be measured using the screen monitor at the end of the diagnostic beamline.
The energy distribution can be controlled by adjusting the RF phases in Sectors 3–5.
During operation, beam diagnostics can be performed using a test beam mode copied from the KBE mode (Rep. rate ≤ 1 Hz)
Issue: Radiation-induced camera failures and degradation
 Improved radiation shielding is required
Energy distributions at different upstream RF (sector 3-5) phases, and energy spread as a function of upstream RF phase.
Screen: SC_61_A3

## Slide 7
 | E3730A | MBK (KMS80)
Power : MW | 50 | 80
Efficiency : % | 45 | 70
# of Beam | 1 | 8
Perveance(10^-6). | 2.1 | 2.2 (0.27×8)
Cathode V : kV | 312 | 304
Cathode I : A | 362 | 376
Gain Min: dB | 51 | 51
Pulse width (RF): us | 4.0 | 
Rep rate :pps | 50 | 
RF Power: 71 MW
MBK
Test Stand
New development: Multi-beam Klystron
We are developing klystrons to achieve high efficiency and high output power. Although the beam power is at the same level as that of conventional models, the output will be 80 MW due to improved efficiency.
We have already begun RF conditioning and have confirmed an output of 71 MW.
A higher accelerating voltage can be achieved with lower RF power
T. Natsui
S. Wang

## Slide 8
Summary
Electron Gun
The RF gun upgrade during the 2026 summer shutdown enabled operation with the input pulse width at its design value.
An improvement in beam quality is expected, particularly for the second bunch compared with the 2026ab run.
HER BT ECS
Although the design RF power could not be applied due to discharges in the waveguide, the energy spread was successfully reduced to nearly the required level.
The installation of an RF contactor in summer 2026 is expected to allow higher RF power.
RF conditioning and beam studies will begin in the 2026c run.
Fast Kicker
The fast kicker contributed to stable injection of the second bunch.
Countermeasures against electrical discharges have been implemented.
Radiation shielding is being designed for areas with high radiation dose rates.
SR Monitor at SY3
Non-destructive monitoring of electron and positron beams at the end of the LINAC has become possible.
The monitor is also expected to be useful for positron beam tuning.
SY3 Beam Diagnostic Line
The diagnostic line allows a portion of the electron beam to be sampled and directed to the diagnostic line for direct measurement of the energy spread.
It was confirmed that the energy spread can be controlled by adjusting the RF phases in sectors 3–5.
The camera frequently stops functioning due to beam losses at the dispersive section near the screen monitor and radiation from the beam dump.
Radiation shielding needs to be designed and implemented.
New development: Multi-Beam Klystron (MBK)
A high-efficiency klystron has been successfully developed as part of the injector upgrade program.
The MBK achieves an efficiency of 70%, compared with 45% for conventional klystrons.
High-power testing is progressing smoothly.
More stable operation and higher accelerating gradients are expected.

## Slide 9
Current / Injection
F. Miyahara for Current/Injection Task force

## Slide 10
Challenges of the Current/Injection Task Force
We aim to improve injection beam quality and injection efficiency, and increase beam current to achieve higher luminosity.
Collaborative efforts among optics and hardware experts are important to improve performance and resolve outstanding issues.
Members of the Optics, Hardware, and Belle II teams are working together to address these challenges.

## Slide 11
Current Status

## Slide 12
Injection Status
0
1
2
3
0
5
10
50
0
0
100
500
1000
1500
HER
LER
HER/LER
Current [mA]
Injection Efficiency [%]
Bunch Charge
at Gun Exit [nC]
Bunch Charge
at BT END [nC]
Maximum beam current LER: 1650 mA, HER: 1300 mA
During the 2026ab run, injection efficiency improved and could be maintained at a high level, particularly in the HER.
Daily Injection Turning
Emittance Auto Tuning
Automatic Orbit Feedback
The positron beam charge gradually decreased due to a reduction in electron emission from the cathode of the thermionic gun.
The electron beam charge remained stable at 2 nC/bunch.
Successfully achieved stable injection of the second bunch
Beam Current
Injection Beam Emittance
Bunch Current
Power outage: Many devices lost their calibration
e+: 1st
e+: 2nd
e-: 1st
e-:2nd
Luminosity
Luminosity [x 1034 cm-2s-1]

## Slide 13
Injection Status: Injection Efficiency
e- 1st (100th turn)
e- 1st (Next Inj.)
e- 2nd (100th turn)
e- 2nd (Next Inj.)
e+ 1st (100th turn)
e+ 1st (Next Inj.)
e+ 2nd (100th turn)
e+ 2nd (Next Inj.)
From the 2026ab run, the injection efficiency calculated from the bunch current at the timing of the next injection cycle has also been measured and archived.
Bunch Current Monitor [mA]
Injection
Next Injection Cycle
Num. of shots from injection
H. Kaji
Injection efficiency 100 turns after injection
HER
LER
Injection efficiency at the next injection timing
Depends on
Injection beam quality (e, sE)
Injection tuning (Septum, Kicker)
Injection efficiency at the next injection
Depends on MR condition (tune, Collimator, …)
The net injection efficiency is the injection efficiency at the next injection timing.
Improving injection efficiency measured at next injection is also important.

## Slide 14
Required Parameters and Current Status: Bunch Charge at BT END
Electron Beam
Target: 3 nC
Targett: 4 nC
LINAC END : 1st / 2nd
BT END: 1st / 2nd
Previously operated at 2 nC.
Confirmed 4 nC beam extraction from the electron gun.
Currently optimizing and verifying the generation and transport of low-emittance beams at high bunch charge.
Positron Beam
SY2
Increased the grid
pulser pulse width
1014 nC @Gun Exit
1st @ Gun
2nd
1st
Cathode emission current has been gradually decreasing.
In 2026ab, positron capture was optimized to maximize transmission efficiency to the DR  The bunch charge at BT remained constant of 2.5 nC
Extended the grid pulser pulse width to increase the bunch charge Gun Exit: 1014 nC SY2 (BT to DR Entrance): 3.9  4.9 nC  Currently conducting beam tests up to SY2.
Beam tests up to DR-BT are scheduled for December.
2nd @Gun
Detail: Electron gun/Positron source talk (Zhou-san).
1st @ Gun
2nd @Gun
New gun
(now)

## Slide 15
 | 1st only | 1st+2nd | 1st+2nd （energy adjusted） | Requirement
e- | 0.033% | 0.076% | 0.074% | 0.07%
e+ | 0.058% | 0.069% | 0.067% | 0.16%
Required Parameters and Current Status: Energy Spread
Y. Seimiya
Current Energy Spread and Required Specifications
The electron beam energy spread is close to the required value.
Phase drifts in the downstream LINAC can occasionally cause the energy spread to exceed the required limit.
The input RF power was limited by discharges at the waveguide flange, but a countermeasure was implemented in the summer of 2026 by installing an RF contactor.
Increase the ECS accelerating gradient to further reduce the energy spread.
The energy spread of the positron beam is sufficiently small
Electron Beam
Positron Beam

## Slide 16
Required Parameters : Emittance of the Injection Beam
e- 2026ab | BT1 | BT2 | Req.
gex [mm] | 104±2 | 233±11 | 40
gey [mm] | 52.8±1.6 | 135±7 | 20
e+ 2026ab | BT1 | BT2 | Req.
gex [mm] | 119±2 | 207±9 | 100
gey [mm] | 5.4±0.4 | 47±2 | 15
N. Iida
Significant emittance blowup from BT1 to BT2 is a major issue for both e- and e+ beams
BT1
BT2

## Slide 17
Emittance Blow-up in BT
 Mori-san’s talk
One of the highest-priority issues

## Slide 18
by* | Action | Injected beam | Ring Acc.
0.9 | 2Jx [mm] | 1.01 < | 1.4
 | 2Jy [mm] | 0.059 >> | 0.038
1.0 | 2Jx [mm] |  | 1.7
 | 2Jy [mm] |  | 0.037
by* | Action | Injected beam | Ring Acc.
0.9 | 2Jx [mm] | 1.48 >> | 1.15
 | 2Jy [mm] | 0.036(6s) < | 0.044
1.0 | 2Jx [mm] |  | 1.65
 | 2Jy [mm] |  | 0.04
2026ab
2026ab
by* | Action | Injected beam | Ring Acc.
1.0 | 2Jx [mm] | 0.95 ~ | 0.90
 | 2Jy [mm] | 0.060(6s) >> | 0.04
by* | Action | Injected beam | Ring Acc.
1.0 | 2Jx [mm] | 1.29 ~ | 1.4
 | 2Jy [mm] | 0.062(6s) >> | 0.025
2024c
2024c
HER
LER
N. Iida
Betatron Oscillation Amplitude and Ring Acceptance
HER: Vertical Emittance is Critical
LER: Horizontal Emittance is Critical

## Slide 19
Emittance Automatic Tuning

## Slide 20
Laser-RF relative phase and Injection Efficiency
Objectives: Identify the factors causing variations in beam emittance and injection efficiency
SRM beam size variations and injection efficiency degradation are often associated with vertical orbit deviations just downstream of the electron gun
Upstream orbit changes induce kicks on the bunch tail
Relative phase between Laser and RF affects the beam orbit
A correlation was observed between the upstream beam orbit and injection efficiency
No clear correlation is observed downstream, presumably because orbit feedback maintains stable beam conditions.
1) Beam orbit and Injection Efficiency

## Slide 21
Laser phase
y position at J-ARC entrance
2,3) Effect of Laser-RF relative phase on the beam orbit and Wakefield-induced kicks
Beam position changes with laser phase (top) and beam profile measured at the center of J-ARC with an applied energy chirp (bottom). The horizontal axis is converted to an approximate time scale.
Wakefield-induced kicks on the bunch tail when the beam orbit deviates from the optimal operating orbit (DfLaser = 2.5, 5 deg).
head
tail
Varied the laser phase to observe beam orbit changes
Applied an energy chirp in Sector-B to measure the longitudinal (time) distributions
Energy chirp
Screen Monitor
The laser–RF relative phase affects beam emittance.
It also affects energy spread by shifting the beam phase relative to the accelerating RF.
Adjusting the relative phase between the laser and RF is required to maintain low emittance

## Slide 22
Emittance Auto Tuning (EAT)
Objective function:
/
/
/
: Horizontal / Vertical Beam size at SRM i (i = 0, 1)
: Horizontal / Vertical b function at SRM i
: Bunch charge at Gun eixit / Linac end
w : Weighting factor (w=2) to emphasize vertical emittance
Y. Seimiya
Optimize the beam orbit to minimize the beam sizes measured at two SRMs
In two-bunch operation, this also minimizes the overlap of the two bunches, leading to an overall improvement in injection efficiency
Objective: Add the adjustment of the relative phase between the laser and RF to the EAT
Upgrade of EAT

## Slide 23
Injection efficiency improvement through Emittance Auto Tuning
Include the overall LINAC RF phase in Emittance Auto-Tuning (EAT)
Improved injection efficiency and reduced Belle II background with RF Phase Adjustment and Emittance Auto Tuning.
EAT operation
EAT with RF phase
optimization
EAT and RF phase optimization significantly improved HER injection efficiency and reduced the Belle II background.
A reduction in beam emittance in the BTe was confirmed.
Future Improvements
Optimization of energy spread with SY3 beam diagnostic line
Implement automatic tuning of the 2nd bunch using the Fast Kicker
Using the new SR Monitor at SY3
Y. Seimiya
Vertical emittance at BT1 has been significantly reduced.
2nd
1st bunch
Comparison of emittance before and after the introduction of EAT
Emittance blowup between BT1 and BT2 remains a major challenge.
Blowup

## Slide 24
Automatic Orbit Feedback

## Slide 25
Reconstruction of the BT simulation Model and Implementation of Automatic Orbit Feedback
Measure the orbit response function (displacement per unit kick angel) and dispersion function
Evaluate the normal and skew quadrupole field errors required to reproduce the measured response in SAD simulations.
Response Function Measurement and Model Reconstruction
Comparison of measured and simulated injection beam orbit
Horizontal (before)
Vertical (before)
Hor. (After field error cor.)
Ver. (After field error cor.)
Magnetic field errors of individual Quadrupoles(Top: Before correction; Bottom: After Correction)
Automatic Correction
Calculate the steering kick angles required to correct the orbit deviations from the golden orbit.
Y. Shimosaki
?
Objectives: Compare model predictions with measurements and Stabilize the injection beam orbit
Large error
Cause unknown
before
after field error correction

## Slide 26
FB ON
FB ON
FB ON
ECS
Automatic Orbit Feedback in BTe
Large beam orbit fluctuations
Stable after FB implementation
(Steps correspond to changes in the golden orbit, etc.)
Y. Shimosaki
Long-term beam orbit drift was eliminated, and orbit jitter was significantly reduced

## Slide 27
Automatic Orbit Feedback in BTp
Y. Shimosaki
Positron beam orbit is also stabilized
FB ON
FB ON
FB ON
In the LER, since correcting for field errors stil resulted in large discrepancies between simulations and experiments, orbit correction is performed using the measured response matrix.

## Slide 28
Long-term beam orbit drift was eliminated, resulting in stable injection efficiency
Injection stability was greatly improved
Enabled practical use of collimators (Studies are planned for the next operation period)
Future Improvements
Improve FB accuracy and stability by increasing the number of BPMs (BPM signal overlap issue is resolved) and optimizing BPM and steering magnet selection
Investigate the causes of large magnetic field errors
Automatic Orbit Feedback and Injection Stability
FB ON
Implementation of Automatic Orbit FB

## Slide 29
Increase in Positron bunch charge

## Slide 30
Increase in Positron bunch charge
At the thermionic gun exit
e+ Capture Section  SY2 (entrance of Linac To Damping Ring BT)
Detail will be presented tomorrow by Zhou-san.
There are more than 100 DC quadrupole magnets, and their settings cannot be changed during PF operation. Due to the time-consuming tuning process, optimization to increase the transmission efficiency had been performed only once before this Octber.
 In this October this year, we performed optimization again.
DC magnet optimization in this section
T. Natsui
SY2

## Slide 31
 | Qtarget [nC] | Transmission: 15T28_4
2026/1 | 9 | 45%
2026/10 | 8.3 | 51%
Positron target:
Q(SP_15_T)
SY2 entrance:
Q(SP_28_4)
Target-to-SY2 transmission increased by 6% relative to 2026ab.
Optimization of Positron Production and the Downstream Section of the Capture Section
Optimization including the BT from SY2 to the DR is planned for December
Optimize the capture phase in the Capture Section and the magnets downstream of SY2.

## Slide 32
HER Synchrotron Injection

## Slide 33
Betatrotron injection (BI)
Off axis, on momentum
Synchrotron injection (SI)
On axis, off momentum
Injection point
Dx
Dx
Extraction region
Extraction region
Injection point
Dispersion
Dispersion
Inj. orbit
Inj. orbit
hx=DX/d: horizontal dispersion=orbits of the beam with offset energy (d)
In SI, the energy of injection beam is made 0.6% higher = The injection beam’s orbit makes the dispersion orbit.
In the non-dispersive region. → DX=0 at the interaction region. → However, although it oscillates in the longitudinal direction, its impact on collisions is small.
In SI, the horizontal betatron injection oscillation is replaced by longitudinal synchrotron oscillation by utilizing the horizontal dispersion and an energy offset of the injected beam
 | BI | SI
Beam-beam kick at IP | Large H. oscillation | No H. oscillation
Beam-beam with nano-beam | H. osci. causes shift of s→large by | (Coll. at s~10sz)
Dynamic aperture (DA) | Large H. osci. decreases V. DA | No H. osci.
SR to the IP beam pipe | Larger due to H. osci. | No H. osci.
Damping time | 58 ms (Horizontal) | 29 ms (Longitudinal)
Sensitivity to b-b, sext. misalignment, and tune | More sensitive | Less sensitive
The horizontal phase space at the injection point
Optics and orbits in the injection region
Comparisons of the betatron injection(BI) and synchrotron injection (SI)
N. Iida
Why synchrotron injection

## Slide 34
Measured beam oscillations using TbT-BPMs with the detuned optics
Betatron injection
Synchrotron injection
Number of turns
Number of turns
Q [nC]
y [mm]
x [mm]
Q [nC]
y [mm]
x [mm]
FFT(s)
FFT(y)
FFT(x)
FFT(s)
FFT(y)
FFT(x)
Fractional tune
Fractional tune
Simulations (by*=1mm, w/o collimators, knobs, b-b, and different tune)
K. Oide
Frequency components
The SI was tested from Nov.6 to 20 in 2025.
Comparison of ten-minutes operation with the by*=1 mm optics
Inj. Eff. ~20%
A peak appears in the frequency spectra at the horizontal tune in BI, while the synchrotron tune in SI. These results indicate a perfect realization of the synchrotron injection as the simulation results.
nx=.535
ns=.0277
N. Iida
Inj. Eff. ~60%
The injection efficiency of SI reached 60% after 7.5hr-tuning, on the other hand, that of BI stayed only 20% after 4 days.
In 2026ab, the injection efficiency reached 60% even with BI, thanks to Emittance Auto-Tuning and injection optimization.
We aim to evaluate the effect of Synchrotron Injection under the same injected beam conditions.
The test was terminated after a short period because:
Beam injection onto adjacent RF buckets occurred, and the cause could not be identified. (This had also occurred during BI, but only rarely)
Changin the rep. rate from 5 to 12.5 Hz increased the background
The physics run was scheduled immediately afterward.
Injection tuning is easier because it is less sensitive to the tune and sextupole misalignments, etc.
Injection Comissioning

## Slide 35
Parameters Required for Luminosity of 1x1035 and Future Plans

## Slide 36
Parameters Required for Luminosity of 1x1035
 | Spec. Lum. Case A Based on the Maximum Spe. Lum. Archived in 2026ab |  | Spec. Lum. Case B by*=0.8 and 112.5% of Case A | 
 | LER | HER | LER | HER
Luminosity [1035cm-2s-1] | 1 |  | 1 | 
Nb | 2746 |  | 2346 | 
Total beam current [mA] | 3033 | 2426 | 2365 | 1892
Bunch current [mA] | 1.104 | 0.8835 | 1.008 | 0.8066
Bunch current product [mA2] | 0.9758 |  | 0.8133 | 
Specific luminosity [1031cm-2s-1mA-2] | 3.732 |  | 5.241 | 
by* [mm] | 0.9 |  | 0.8 | 
Lifetime [min.] | 4.29 | 11.3 | 5.11 | 12.4
Loss rate [mAs-1] | 11.8 | 3.58 | 7.71 | 2.55
Injection rate [mAs-1] # | 4.19 | 3.16 | 5.12 | 4.37
Y. Funakoshi
# Assumption: e+/e- Bunch charge = 3 nC, Beam Rep. Rate: LER 23 Hz, HER 25 Hz
One Model Scenario: Model-Dependent Due to the Unexplored Beam Current Regime
Parameters Required to Achieve a Luminosity of 1 x 1035, and Expected Loss and Injection Rates, Based on Measured Injection Efficiency, Beam Lifetime, and Specific Luminosity in 2026ab
In the LER, the beam loss rate significantly exceeds the injection rate.
The situation is also challenging for the HER.

## Slide 37
Hardware Upgrade

## Slide 38
Requests to the Hardware Group
Requests for Hardware Improvements to Enhance Injection Efficiency, Reduce Injection Background, and Investigate Issues Such as Emittance Growth
Installation of New Synchrotron Monitor at SY3 and the LER BT
A new SRM has been installed at SY3.
Tests to integrate the new SRM into automated emittance tuning are planned to begin in December.
R. Zhang, Y. Okayasu
No SRM has been installed in the LER BT yet.

## Slide 39
Addressing BT BPM Issues and Improving Performance
Issue1: Abnormal oscilloscope trigger timing in the BT BPM system caused missed beam measurements and timing shifts.
timing shift
missed beam
measurements
e+ Bunch Charge at the LINAC END and BT BPM before timing correction
e+ Bunch Charge at the LINAC END and BT BPM After timing correction
Fixed
Radiation Protection for the SY3 Beam Diagnostic line Camera
Frequent camera shutdowns due to radiation from the beam dump prevent stable measurements.
Radiation shielding upgrades were postponed from the summer shutdown to the next shutdown due to higher-priority work, including SRM installation.

## Slide 40
Issue2: BPM Signal Overlap and Poor Position Resolution
QXF1P_A_1
QWFP_4A_1
(LER)
R1
R2
QWDP_2A_1
QXD1P_A_1
QXD5P_K_1
QWFP_3A_1
QXF5P_K_1
QXD2P_A_1
QXD6P_K_1
QWDP_3A_1
QXF2P_A_1
QAD5P_A_1
QXF6P_A_1
QAF6P_K_1
QAD7P_A_1
QAF8P_K_1
QWFP_4A_1
QXF1P_A_2
QWDP_2A_2
QXD1P_A_2
QXD5P_K_2
QWFP_3A_2
QXF5P_K_2
QXD2P_A_2
QXD6P_K_2
QWDP_3A_2
QXF2P_A_2
QAD5P_A_2
QXF6P_A_2
QAF6P_K_2
QAD7P_A_2
QAF8P_K_2
QWFP_4A_2
R3
R4
0.1 ns/point
CH1
CH2
CH3
CH4
Fewer BPMs provide valid measurements during double-bunch operation.
Limited BPM availability for orbit feedback.
Few BPMs can measure both bunches, requiring orbit comparisons using different BPMs for the 1st and 2nd bunches.
BPM resolution-induced position spread exceeds orbit jitter, making it difficult to identify the underlying problems.
Detail will be presented in this afternoon’s Control/Monitor session (Ikeda-san’s talk).
Overlap of the BPM raw signals.
1st bunch
2nd bunch
An issue that complicates beam operation and root cause investigation.

## Slide 41
LER Injection Point Chamber Upgrade
Enlarge the aperture on the stored beam side of the Q-magnet chamber at the injection point
Increase the kicker height to reduce the separation between the injected and stored beam, thereby reducing the amplitude of injection oscillations
An injection-point chamber with an enlarged aperture will be installed in December
Starting Point of the recess
Machine 1 mm deeper
1 mm
This part will be widened

## Slide 42
Challenges for Luminosity Improvement
Worse than in 2022  Investigate the cause (Ground subsidence? Magnet misalignment?)
Investigate the cause of the decrease in Specific Luminosity at high beam currents
In 2024ab, The beam injection efficiency dropped at by=0.8  Search for better operating condition?
Specific Luminosity
Beam Lifetime
Injection Efficiency / Rate
Beam-gas Coulomb  Improvement of Vacuum Pressure
Touschek  Optimization of Dynamic Aperture (Sextupole Optimization)
Crab waist ratio Optimization
Injection beam emittance  Reduction of Initial Emittance (RF-gun?) Investigation of the Cause of Emittance Blow-up in BT and its Mitigation
Injection efficiency degradation along the train  Investigation of the Cause (Beam loading?, Tune?)
Increase in Charge  Attemp to transport a Low-Emittance Beam during the 2026c and 2027a Runs
Improved Automatic Orbit Feedback Precision Following the BT BPM Upgrade  In Later Slides and the Control/Monitor Talk (Ikeda-san)
Improved Emittance Auto Tuning (EAT) with SY3 beam diagnostics line, following the BT BPM Upgrade

## Slide 43
Challenges:
Confirm compliance with internal beam loss and radiation limits.
Review the limits with the Radiation Science Center if necessary.
Measure the radiation dose at the injection kicker power supply downstream of the collimators and evaluate the risk of radiation damage.
Planned Measurements
Radiation levels at critical locations (Radiation Science Center).
Collimator position vs. beam charge (beam profile scan).
Long-term beam loss stability.
Gamma-ray and neutron dose at the kicker power supply.
Collimator position vs. injection background.
Why Haven’t we used the Collimators? Large orbit drifts previously prevented collimator use.
However, successful orbit feedback now makes collimator operation feasible
Injection Background
High Injection Background 
Objective: Remove beam halo and energy tails using collimators at SY3 and in the BT before injection
to Reduce Injection Beam-Loss Background
Reduce DAQ Efficiency Due to Injection Veto
MR Beam Current Limited by Increased Injection and Storage Background

## Slide 44
Summary
HER/LER Beam Current
During the 2026ab run, the beam currents reached 1650 mA for the LER and 1300 mA for the HER.
Further increases in beam current are planned starting from the 2027a run (see Mitsuka-san's talk).
Challenges:
Beam lifetime currently limits the achievable beam current.
To reach a luminosity of \(10^{35}\), it is necessary not only to increase the injection power but also to reduce the beam loss rate.
Beam loss between successive injections (the difference between the injection efficiency at the 100th turn and that of the next injection) needs to be reduced.
For SBL, see Uno-san's talk.
Injection Beam Charge
During the 2026ab run, injection beam charges of 2 nC for the HER and 2.6 nC for the LER were achieved.
Higher bunch charges are expected through the RF gun upgrade and an increase in the pulse width of the thermionic electron gun.
Beam studies with higher bunch charges will begin in the 2026c run.
Injection Background Mitigation
We plan to reduce injection background by cutting the energy and emittance tails using collimators in SY3 and the HER/LER BT lines.
It is necessary to evaluate the constraints imposed by radiation dose limits at KEK and the risk of radiation damage to the kicker power supplies downstream of the collimators.
Beam studies will begin in the 2026c run.

## Slide 45
Injection Beam Emittance, Energy Spread, and Beam Stability
Electron
Emittance Auto Tuning (EAT) and Automatic Orbit Feedback have enabled stable injection of low-emittance beams.
Stable injection of the second bunch into the HER has been achieved.
The gun upgrade is expected to improve the second-bunch quality to a level comparable to that of the first bunch.
We will further improve EAT and Automatic Orbit Feedback using the SRM at SY3, the upgraded BT BPMs, and the SY3 diagnostic line, aiming to reduce the emittance at the BT end.
The ECS can now compress the energy spread to the required level. However, the accelerating gradient is lower than the design value, leaving little margin relative to the requirement.
Higher RF power is expected to become available after addressing the waveguide discharge issue. Beam studies will begin in the 2026c run.
Positron
- Automatic Orbit Feedback has enabled stable beam orbit control from the DR to injection.
Common Challenges
Emittance blow-up in the BT remains a major bottleneck. Identifying its cause and implementing countermeasures are urgent priorities.
The upgraded BT BPMs are expected to facilitate further investigation of this issue.
Synchrotron Injection
Synchrotron injection successfully suppressed injection oscillations, making injection tuning easier.
Due to limited beam study time, a detailed comparison with betatron injection could not be completed.
We plan to make the necessary preparations and perform a more detailed comparison in a future beam study.

## Slide 46
Appendix

## Slide 47
Thermionic Gun Heater Current and Bunch Charge

## Slide 48
Name | date | Status | Notes
FY_A2_2 | 2024/8 | Operation | Polarity Reversed，Capacitor: 40 μF  8 μF
FY_A4_4 | 2024/8 | Operation | Capacitor: 40 μF  8 μF
FY_R0_2 | 2022/8 | Shut down | Enhanced shielding is required
FY_48_4 | 2026/4 | Ope.  failure | Improving the High-Voltage Withstand Capability of Litz Wire. Capacitor: 40 μF  8 μF
FY_58_4 | 2025/8 | Operation | Enhanced shielding is required
To avoid the risk of damaging the high-speed switching module (¥1.6 million) due to hard switching (high induced voltage), the capacitance was reduced to achieve soft switching. However, soft switching increased the overshoot amplitude, so the introduction of a diode is being considered. In the current configuration, the 1st and 2nd bunches can be kicked in opposite directions, with sufficiently good waveform reproducibility.
On June 22, 2026, an electrical discharge occurred in the Litz wire of FY_48_4, and the cable was replaced. However, another discharge occurred on July 1, leading to the suspension of operation. The voltage withstand capability of the Litz wire was improved
Shielding for FY_R0_2 and FY_58_4 is currently being designed using PHITS.
Hard switching
Soft switching
Current
Trigger
Fast Kicker: Operational use began in the 2026ab run
Y. Okayasu, T. Natsui
Fast Kicker led to stable injection of the second bunch.

## Slide 49
BTp simulation Model and Automatic Orbit Feedback
In the LER, since correcting for field errors stil resulted in large discrepancies between simulations and experiments, orbit correction is performed using the measured response matrix.
Example of an orbit

## Slide 50: Injection Commissioning
Measured beam oscillations using TbT-BPMs with the detuned optics
Betatron injection
Synchrotron injection
Number of turns
Number of turns
Charge
[nC]
y [mm]
x [mm]
Charge
[nC]
y [mm]
x [mm]
FFT(s)
FFT(y)
FFT(x)
FFT(s)
FFT(y)
FFT(x)
Fractional tune
Fractional tune
Simulations (by*=1mm, w/o collimators, knobs, b-b, and different tune)
K. Oide
Frequency components
The SI was tested from Nov.6 to 20 in 2025.
HER Synchrotron Injection
Dynamic aperturesm(DA) by simulations
Comparison of ten-minutes operation with the by*=1 mm optics
einj~60%
einj~20%
einj~60%
The injection efficiency of SI reached 60% after 7.5hr-tuning, on the other hand,
that of BI stayed only 20% after 4 days. However, after retuning of injection in Feb. 2026, 60% was achieved by BI.
BI
SI
x-y
z-xy
(a), (b): The transverse dynamic aperture. The orange square indicates ∼ ±2.5σ of the injected beam. As for SI(b), the tracking starts with an initial momentum offset ∆p/p0 = 0.6 %, the perform a synchrotron motion. . The amplitude ratio Jy/Jx are set at 1 %.
(c), (d): The dynamic momentum acceptance are plotted in (c) BI and (d) SI, respectively, where the horizontal axes are the initial momentum offset. The orange squares show the horizontal size and momentum spread of the injected beams.
Possibility of larger off-momentum DA, see Koga-san’s talk tomorrow.
A peak appears in the frequency spectra at the horizontal tune in BI, while the synchrotron tune in SI. These results indicate a perfect realization of the synchrotron injection as the simulation results.
nx=.535
ns=.0277
K. Oide
N. Iida

## Slide 51
Specific Luminosity
Assumption
-Specific luminosity@by*=0.9 mm
HBC study (2026/6/16)
Red line (Case A): a line tangent to the HBC study data
-Specific luminosity@by*=0.9 mm
HBC study (2026/6/16) * (1-0.125)
Green line (12.5% degrade at high beam currents)
-Specific luminosity@by*=0.8 mm
(Red line * (1 + 0.125))
Blue line (Case B)
-Specific luminosity
Grey line (fit to 2022 data (by*= 1mm))
Y. Funakoshi
Used to evaluate the required parameters

## Slide 52
Specific luminosity: red
Specific luminosity: blue
Case B
Case A
Based on the Maximum Archived in 2026ab
by*=0.8 and 112.5% of Case A
Luminosity as function of LER Current
IHER/ILER = 0.8
IHER/ILER = 0.8
Y. Funakoshi
Used to evaluate the required parameters

## Slide 53
Injection Efficiency model
LER
High beam current collision Study (2026/6/16)
37.52*Log
HER
Used to evaluate the required parameters
Y. Funakoshi

## Slide 54: Beam Lifetime model (LER)
LER: Touschek and vacuum lifetime is considered.
= 1600 mA, = 2249, 5.7 x 10-8Pa
-> = ~7.4min. (Touschek: 14.8 min., Vac: 14.8 min.)
=0.0950 [mA-1・min-1], 4.223e-5 [mA-1・min-1]
Itotal [mA]
Beam lifetime [min.]
Nb = 2053
G. Mitsuka
5.7 x 10-8Pa@1600mA
Data during beam collisions
Current [mA]
Used to evaluate the required parameters
Y. Funakoshi

## Slide 55: Beam Lifetime model (HER)
HER: Touschek lifetime is considered.
= 1300 mA, = 2346 -> = ~18min.
=0.1003 [mA-1・min-1]
Itotal [mA]
Beam lifetime [min.]
Nb = 2346
G. Mitsuka
Data during beam collisions
Current [mA]
Used to evaluate the required parameters
Y. Funakoshi